## Slide 1: Direct Memory Access (DMA)
Feb 02, 2023

## Slide 2: What is DMA?
DMA is a technology that allows data to be transferred directly from one memory location to another without the involvement of the CPU. This results in a significant improvement in the system's performance, as the CPU is freed up to perform other tasks while the DMA controller handles the data transfer.
In a DMA system, there are three main components: the CPU, the memory, and the DMA controller. The CPU initiates the transfer request and specifies the source and destination addresses in memory. The DMA controller then takes over, reading the data from the source memory location and writing it to the destination memory location.
The DMA controller has a dedicated channel for each peripheral device that needs to transfer data. Each channel has its own set of registers for specifying the source and destination addresses, as well as the transfer count and other control parameters. The DMA controller also has a dedicated bus interface to the memory, allowing it to access memory directly without the need for the CPU to be involved.
In conclusion, the DMA architecture provides a way for peripherals to transfer data to and from memory without involving the CPU, thereby improving system performance and efficiency.
CPU
DMA Controller
Memory
I/O device
I/O device
I/O device
AXI bus
AXI bus without DMA

## Slide 3: How DMA works?
How a DMA transfer works:
The peripheral device initiates a DMA transfer request.
The CPU sets up the source and destination addresses in memory and the number of bytes to be transferred, and then gives control to the DMA controller.
The DMA controller takes over, reading the data from the source memory location and writing it to the destination memory location, without involving the CPU.
Once the transfer is complete, the DMA controller signals of the peripheral device and the CPU that the transfer is done.
CPU
DMA Controller
Memory
I/O device
I/O device
I/O device
AXI bus
Handshake
Handshake
Data
Master interface
Master interface
Slave interface

## Slide 4: DMA controller block diagram
A DMA block diagram consists of the following components:
DMA Controller: The heart of the DMA, this component manages the entire data transfer process and is responsible for scheduling the transfers, calculating the transfer addresses, and generating the control signals.
AXI interface unit (AXI_IU): This component is responsible for interfacing with the system bus, specific is AXI bus.
Direct Memory Access Channel (DMAC): There can be one or more DMACs, depending on the number of peripheral devices that need to be supported. Each DMAC is responsible for a specific data transfer, and it communicates with the DMA controller to receive transfer instructions and control signals.
Address Generation Unit (AGU): The AGU generates the memory addresses for the data transfer, and it can also perform address calculations for scatter/gather operations.
Direct Memory Access Transfer Unit (DTU): This component is responsible for performing the actual data transfer, reading the data from the peripheral device and writing it to the memory or vice versa.
Peripheral Interface Unit (PIU): This component is responsible for interfacing with the peripheral device, and it provides the necessary control signals and data signals to initiate and control the data transfer.
I/O device
I/O device
AXI_IU
DMAC
AGU
DMA Controller
DTU
PIU
CPU
Memory
AXI bus
I/O device
Master interface
Master interface
Slave interface
Handshake
Data
Handshake
DMA controller
 | Control path
 | Data path